Display RGB 8x6
communication protocol
Version 1.0

# 1. Introduction
Тhe device consists of several modules with RGB matrix of 8 x 6 pixels. Number of modules is determined by the number of rows and number of modules in one row.
This document explains communication with display via UART.
# 2. UART communication parameters and coding system
## 2.1. UART communication parameters
- Communication standard: RS485 half duplex
- Data transmission speed: 250Kbps
- Serial protocol: 8-N-1 (8 data bits, no parity bit, 1 stop bit)
## 2.2. Connector for RS485 communication
For RS485 communication is used RJ45 connector.
Pins assignment:
- 1-3: power supply (from +5V to + 8V)
- 4: RS485 B inverting input or output
- 5: RS485 A non inverting input or output
- 6-8: power and signal ground
## 2.3. Coding system
Communication is done through the frames of data.
Data in frame are coded with Hamming code.
The length of coded frame is 22 bytes, and length of decoded frame is 8 bytes.
Value of fixed bytes in coded frame:
#define FRAME_LENGTH	0x16	// Coded data
#define DATA_LENGTH	0x08	// Decoded data
#define FRAME_START	0x81
#define FRAME_TYPE_COMMAND	0x7E
#define FRAME_TYPE_ACK	0xE7
#define FRAME_TYPE_REPLY	0xEE
#define FRAME_STOP1	0xBD
#define FRAME_STOP2	0xDB
First byte in coded frame is FRAME_START = 0x81, 21-st byte is FRAME_STOP1 = 0xBD, and 22-nd byte is FRAME_STOP2 = 0xDB.
Second byte determines type of frame.
- FRAME_TYPE_COMMAND = 0x7E – command
- FRAME_TYPE_ACK = 0xE7 – acknowledgment of command
- FRAME_TYPE_REPLY = 0xEE - response to the command
Bytes from 3-rd to 20-th are coded values of 8 data from command, including two check-sum bytes into positions 19 and 20. Check_sum is sum of 8 command bytes increased by 7. For each byte from command exists two coded bytes in coded frame.
There is source code (C language) for coded data frame calculation
unsigned char coded_data[22];
unsigned char data[8];

void CodeFrame(unsigned char frame_type, unsigned char *data, unsigned char *coded_data)
{
unsigned char Haming84[] = { 0x00, 0x87, 0x99, 0x1E, 0xAA, 0x2D, 0x33, 0xB4,
0x4B, 0xCC, 0xD2, 0x55, 0xE1, 0x66, 0x78, 0xFF };
unsigned char i, j, temp, check_sum;
coded_data[0] = FRAME_START;
coded_data[1] = frame_type;
coded_data[20] = FRAME_STOP1;
coded_data[21] = FRAME_STOP2;
check_sum = 7;
j = 2;
for (i = 0; i < 8; i++)
{
sum += data[i];

temp = Haming84[data[i] >> 4];
coded_data[j++] = temp;
temp = Haming84[data[i] & 0x0F];
coded_data[j++] = temp;
}
temp = Haming84[check_sum >> 4];
coded_data[18] = temp;
temp = Haming84[check_sum & 0x0F];
coded_data[19] = temp;
}

There is decoding of coded data frame source code
unsigned char Hamming841[] =
{ 0x00, 0x80, 0x80, 0x41, 0x80, 0x41, 0x41, 0x81, 0x80, 0x42, 0x44, 0x88, 0x49,
0x85, 0x83, 0x41, 0x80, 0x42, 0x4A, 0x86, 0x47, 0x8B, 0x83, 0x41, 0x42,
0x82, 0x83, 0x42, 0x83, 0x42, 0x03, 0x83, 0x80, 0x4C, 0x44, 0x86, 0x47,
0x85, 0x8D, 0x41, 0x44, 0x85, 0x84, 0x44, 0x85, 0x05, 0x44, 0x85, 0x47,
0x86, 0x86, 0x06, 0x87, 0x47, 0x47, 0x86, 0x8E, 0x42, 0x44, 0x86, 0x47,
0x85, 0x83, 0x4F, 0x80, 0x4C, 0x4A, 0x88, 0x49, 0x8B, 0x8D, 0x41, 0x49,
0x88, 0x88, 0x08, 0x89, 0x49, 0x49, 0x88, 0x4A, 0x8B, 0x8A, 0x4A, 0x8B,
0x0B, 0x4A, 0x8B, 0x8E, 0x42, 0x4A, 0x88, 0x49, 0x8B, 0x83, 0x4F, 0x4C,
0x8C, 0x8D, 0x4C, 0x8D, 0x4C, 0x0D, 0x8D, 0x8E, 0x4C, 0x44, 0x88, 0x49,
0x85, 0x8D, 0x4F, 0x8E, 0x4C, 0x4A, 0x86, 0x47, 0x8B, 0x8D, 0x4F, 0x0E,
0x8E, 0x8E, 0x4F, 0x8E, 0x4F, 0x4F, 0x8F, 0x80, 0x40, 0x40, 0x81, 0x40,
0x81, 0x81, 0x01, 0x40, 0x82, 0x84, 0x48, 0x89, 0x45, 0x43, 0x81, 0x40,
0x82, 0x8A, 0x46, 0x87, 0x4B, 0x43, 0x81, 0x82, 0x02, 0x43, 0x82, 0x43,
0x82, 0x83, 0x43, 0x40, 0x8C, 0x84, 0x46, 0x87, 0x45, 0x4D, 0x81, 0x84,
0x45, 0x04, 0x84, 0x45, 0x85, 0x84, 0x45, 0x87, 0x46, 0x46, 0x86, 0x07,
0x87, 0x87, 0x46, 0x4E, 0x82, 0x84, 0x46, 0x87, 0x45, 0x43, 0x8F, 0x40,
0x8C, 0x8A, 0x48, 0x89, 0x4B, 0x4D, 0x81, 0x89, 0x48, 0x48, 0x88, 0x09,
0x89, 0x89, 0x48, 0x8A, 0x4B, 0x0A, 0x8A, 0x4B, 0x8B, 0x8A, 0x4B, 0x4E,
0x82, 0x8A, 0x48, 0x89, 0x4B, 0x43, 0x8F, 0x8C, 0x0C, 0x4D, 0x8C, 0x4D,
0x8C, 0x8D, 0x4D, 0x4E, 0x8C, 0x84, 0x48, 0x89, 0x45, 0x4D, 0x8F, 0x4E,
0x8C, 0x8A, 0x46, 0x87, 0x4B, 0x4D, 0x8F, 0x8E, 0x4E, 0x4E, 0x8F, 0x4E,
0x8F, 0x8F, 0x0F };

// Error codes
#define TERR_BAD_FRAME	0x08
#define TERR_BAD_SUM	0x10
#define TERRB_BAD_CODE	0x05
#define TERRB_NOISE	0x07

unsigned char coded_data[22];
unsigned char decoded_data[8];

unsigned char DecodeFrame1(unsigned char *coded_data, unsigned char *decoded_data)
{
unsigned char i, j, sum, c, data;

if (coded_data[0] != FRAME_START)
return TERR_BAD_FRAME;
if (coded_data[20] != FRAME_STOP1)
return TERR_BAD_FRAME;
if (coded_data[21] != FRAME_STOP2)
return TERR_BAD_FRAME;
j = 2;
sum = 7;
for (i = 0; i <= 8; i++)
{
c = Hamming841[coded_data[j++]];
if (c & WRONG_CODE)
return TERRB_BAD_CODE;
if (c & SINGLE_ERROR)
return TERRB_NOISE;
data = c << 4;
c = Hamming841[coded_data[j++]];
if (c & WRONG_CODE)
return TERRB_BAD_CODE;
if (c & SINGLE_ERROR)
return TERRB_NOISE;
data |= c & 0x0F;

if (i < 8)
{
decoded_data[i] = data;
sum += decoded_data[i];
}
}
if (data != sum)
return TERR_BAD_SUM;
return 0;
}

# 3. Command structure
Command is array of 8 bytes.
Bytes assignment:
- 1 – command code
- 2-3 – device bus ID
- 4-8 – command parameters (5 bytes)
Example:
command code = 0x20
device bus ID = 0x0000
command parameters = {0x10, 0x20, 0x30, 0x40, 0x50}
command data = 20 00 00 10 20 30 40 50
coded command = 81 7E 99 00 00 00 00 00 87 00 99 00 1E 00 AA 00 2D 00 87 B4 BD DB
## 3.1. Communication protocol
- coded command sends from PC or MCU to display (FRAME_TYPE_COMMAND)
- display sends coded acknowledgment of receipt of command (FRAME_TYPE_ACK)
- display sends coded response to command (FRAME_TYPE_REPLY)

# 4. Display setup commands
## 4.1. Set display configuration
Set the number of rows of RGB modules, number of RGB modules in one row (number of
columns), and brightness of display.
Command code is SET_DEVICE_CONFIG = 0x55.
Command parameters:
- P1 – brightness (0 – 100)
- P2 – number of rows of RGB modules
- P3 – number of RGB modules in one row
- P4 – reserve
- P5 – check-sum = P1 ^ P2 ^ P3 ^ P4 ^ 0x3B + 7
Possible responses:
- OPERATION_OK = 0x81
- OPERATION_WRONG = 0x82
Example:
P1 = 10, P2 = 1, P3 = 3, P4 = 0, P5 = 1 0 ^ 1 ^ 3 ^ 0 ^ 0x3B + 7 = 0x3A
Command: 55 00 00 0A 01 03 00 3A
Coded command > 81 7E 2D 2D 00 00 00 00 00 00 D2 00 87 00 1E 00 00 1E 1E FF BD DB
Coded acknowledge < 81 E7 2D 2D 00 00 00 00 00 00 D2 00 87 00 1E 00 00 1E 1E FF BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 00 00 00 00 00 00 00 00 00 CC 00 BD DB
Decoded reply: 81 08 00 00 00 00 00 00
## 4.2. Get display configuration
Get the number of rows of RGB modules, number of RGB modules in one row (number of
columns), and brightness of display.
Command code is GET_DEVICE_CONFIG = 0x56.
No command parameters (all values is 0).
Response is OPERATION_OK = 0x81
Response parameters:
- P1 – brightness (0 – 100)
- P2 – number of rows of RGB modules
- P3 – number of RGB modules in one row
- P4 – 0
- P5 – 0
Example:
Command: 56 00 00 00 00 00 00 00
Coded command > 81 7E 2D 33 00 00 00 00 00 00 00 00 00 00 00 00 00 00 2D 66 BD DB
Coded acknowledge < 81 E7 2D 33 00 00 00 00 00 00 00 00 00 00 00 00 00 00 2D 66 BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 D2 00 87 00 1E 00 00 00 00 CC 78 BD DB
Decoded reply: 81 08 00 0A 01 03 00 00
P1 = 0x0A, P2 = 0x01, P3 = 0x03
## 4.3. Get display versions
Get the display hardware version, and display firmware version.
Command code is GET_DEVICE_VERSION	= 0x57.
No command parameters (all values is 0).
Response is OPERATION_OK = 0x81
Response parameters:
- P1 – HARDWARE_TYPE = 36
- P2 – HARDWARE_VERSION
- P3 – FIRMWARE_VERSION low byte
- P4 – FIRMWARE_VERSION high byte
- P5 – 0
Example:
Command: 57 00 00 00 00 00 00 00
Coded command > 81 7E 2D B4 00 00 00 00 00 00 00 00 00 00 00 00 00 00 2D 78 BD DB
Coded acknowledge < 81 E7 2D B4 00 00 00 00 00 00 00 00 00 00 00 00 00 00 2D 78 BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 99 AA 00 99 00 AA 00 00 00 00 55 D2 BD DB
Decoded reply: 81 08 00 24 02 04 00 00
P1 = 0x24, P2 = 0x02, P3 = 0x04, P4 = 0x00
# 5. Display data commands
## 5.1. Set default color
Default color is used to show the monochromatic image on the display. Brightness also affects to the image.
Command code is SET_DEFAULT_COLOR = 0x5B
Command parameters:
- P1 – red color value (0-255)
- P2 – green color value (0-255)
- P3 – blue color value (0-255)
- P4 – 0
- P5 – 0
Possible responses:
- OPERATION_OK = 0x81
- OPERATION_WRONG = 0x82
Example:
Pure red color is default color
P1 = 0xFF, P2 = 0, P3 = 0, P4 = 0, P5 = 0
Command: 5B 00 00 FF 00 00 00 00
Coded command > 81 7E 2D 55 00 00 00 00 FF FF 00 00 00 00 00 00 00 00 33 87 BD DB
Coded acknowledge < 81 E7 2D 55 00 00 00 00 FF FF 00 00 00 00 00 00 00 00 33 87 BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 00 00 00 00 00 00 00 00 00 CC 00 BD DB
Decoded reply: 81 08 00 00 00 00 00 00
## 5.2. Get default color
Command code is GET_DEFAULT_COLOR = 0x5C
No command parameters (all values is 0).
Response is OPERATION_OK = 0x81
Response parameters:
- P1 – red color value (0-255)
- P2 – green color value (0-255)
- P3 – blue color value (0-255)
- P4 – 0
- P5 – 0
Example:
Command: 5C 00 00 00 00 00 00 00 00
Coded command > 81 7E 2D E1 00 00 00 00 00 00 00 00 00 00 00 00 00 00 33 1E BD DB
Coded acknowledge < 81 E7 2D E1 00 00 00 00 00 00 00 00 00 00 00 00 00 00 33 1E BD DB
Coded reply < 81 7E 4B 87 00 4B 00 00 00 00 FF FF 00 00 00 00 00 00 4B FF BD DB
Decoded reply: 81 08 00 00 FF 00 00 00
P1 = 0, P2 = 0xFF, P3 = 0, P4 = 0, P5 = 0.
Default color is pure green.
## 5.3. Upload monochromatic data to display
One byte represents one column of the RGB module. Bit 0 (lowest bit) represents the bottom
pixel of column, and bit 7 (highest bit) represent the top pixel of column. If value of bit is 1 pixel
will show default color of display, and if value is 0 pixel will turn off. First byte represents first
column (left to right direction).
Command code is UPLOAD_BITMAP_IMAGE = 0x58
Command parameters:
- P1 – number of bytes
- P2-P5 = 0
Response is OPERATION_OK = 0x81
No response parameters (all values are 0)
Example:
Display have 1 row and 3 RGB module in one row. Resolution is 18 x 8. Number of bytes is 18. Image data are : 0xFE, 0x02, 0x02, 0x02, 0x02, 0x00, 0xFE, 0x92, 0x92, 0x92, 0x82, 0x00, 0xFE, 0x82, 0x82, 0x44, 0x38, 0x00.
Command: 58 00 00 12 00 00 00 00
Coded command > 81 7E 00 00 00 00 00 00 2D 4B 00 00 AA 00 66 1E E1 FF AA 87 BD DB
Coded acknowledge < 81 E7 00 00 00 00 00 00 2D 4B 00 00 AA 00 66 1E E1 FF AA 87 BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 00 00 00 00 00 00 00 00 00 CC 00 BD DB
Decoded reply: 81 08 00 00 00 00 00 00
Now PC or MCU sends 18 image data
Image data > FE 02 02 02 02 00 FE 92 92 92 82 00 FE 82 82 44 38 00
Image receiving acknowledge < AA

## 5.3. Upload RGB data to display
Each pixel required 3 bytes if data. Bytes are in order Green, Red, Blue. Values of colors are from
0 to 255.
Order of pixels starts from top left corner, and continues to the bottom of first left column, then
continues to the top of next right column, and so on.
Effective values of color depends of display brightness. Example: if color value is 200, and
brightness is 10, then effective color value is 200 * 10 / 100 = 20.
Command code is UPLOAD_RGB_BITMAP_IMAGE = 0x5D
Command parameters:
- P1 – number of image data low byte
- P2 – number of image data high byte
- P3-P5 = 0
Response is OPERATION_OK = 0x81
No response parameters (all values are 0)
Example:
Display have 1 row and 3 RGB module in one row. Resolution is 18 x 8. Number of bytes is 18 x 8 x 3 = 432.
Command: 5D 00 00 B0 01 00 00 00
Coded command > 81 7E 2D 66 00 00 00 00 55 00 00 87 00 00 00 00 00 00 87 2D BD DB
Coded acknowledge < 81 E7 2D 66 00 00 00 00 55 00 00 87 00 00 00 00 00 00 87 2D BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 00 00 00 00 00 00 00 00 00 CC 00 BD DB
Decoded reply: 81 08 00 00 00 00 00 00
Now PC or MCU sends 432 image data
Image data > G1 R1 B1 G2 R2 B2 … G432 R432 B432
Image receiving acknowledge < AA
# 6. Special commands
These functions are not affect to display's setting and working.
## 6.1. Set relay state
This command switch on relay or switch off relay.
Command code is RELAY_SET_STATE = 0x5A.
Command parameters:
- P1 – relay state (1 – ON, 0 – OFF)
- P2-P5 = 0
Response is OPERATION_OK = 0x81
No response parameters (all values are 0).
Example:
Turn relay on. P1 = 1
Command: 5A 00 00 01 00 00 00 00
Coded command > 81 7E 2D D2 00 00 00 00 00 87 00 00 00 00 00 00 00 00 33 99 BD DB
Coded acknowledge < 81 E7 2D D2 00 00 00 00 00 87 00 00 00 00 00 00 00 00 33 99 BD DB
Coded reply < 81 EE 4B 87 00 4B 00 00 00 00 00 00 00 00 00 00 00 00 CC 00 BD DB
Decoded reply: 81 08 00 00 00 00 00 00
# Revision history
Date	Version	Comment
2016-10-06	1.0	Base document